## Slide 1: SELF charging bot
GROUP MEMBERS:
1) ANIKET HIRDE -14D170006
2) VISHWAS VERMA -140010015
3) KRISHNA KUMAR -140010056
4) HEMANT BODDU -140070046

## Slide 2: PROBLEM STATEMENT
The main goal of the project was to align the solar panel in the direction of maximum light intensity .

## Slide 3: PROBLEM STATEMENT
TO ACHIEVE THIS:
1) The bot will follow white line and reach the defined node where it stops.
2) Next the bot will rotate 360 degrees (5 degrees each), in order to check for the maximum intensity with solar panel inclined to 45 degrees on the axis of right wheel .
3) Then the bot will rotate to the particular angle where the maximum intensity was found in second point.
4) Then the solar panel will ROTATE BY ONE DEGREE IN ORDER TO FIND THE MAXIMUM INTENSITY AND align itself at the angle of maximum intensity. The battery starts charging.
5) After some time(60 seconds) the bot realigns in its position and the same process repeats for further nodes.

## Slide 4: PROJECT VIDEO

## Slide 5: CHALLENGES & SOLUTIONS
Problems we faced are-
(1) Time Delay:
For rotation of bot by 5 degree time delay is 61.9ms (calculated using hit and trial method) AND STABILISATION TIME FOR NEXT ROTATION IS 400ms. Hence total time spent for getting maximum intensity is (61.9+400)*(360/5)=33.25 s.
For rotation of servo by one degree delay time IS 400ms. so total time for one full rotation is 66 s. Hence total time for every 5 degree is 72*66=79.2minutes.
Therefore total time required to check is (79.2 MIN+33.25 S) 80.30 minutes.

## Slide 6: CHALLENGES & SOLUTIONS
SOLUTION:
To overcome this problem we USE A GOOD APPROXIMATION. WE first align the panel at 45 degreeS and rotate the bot UPto 360 AND ALIGN IT AT THE ANGLE AT WHICH THE MAXIMUM VOLTAGE IS RECEIVED.
THEN THE PANEL IS ROTATED AND ALIGNED AT MAXIMUM VOLTAGE.
IN THIS WAY MAXIMUM TIME REQUIRED WOULD BE 3.30 MIN.

## Slide 7: CHALLENGES & SOLUTIONS
2) Maximum voltage that we can give bot is 5V but the panel can generate voltage upto 12V.
SOLUTION: WE USED VOLTAGE DIVIDER CIRCUIT FOR THIS AS SHOWN.HERE WE USED RESISTORS 68 KΩ AND 150 KΩ.

## Slide 8: CHALLENGES & SOLUTIONS
3) The THIRD challenge was measurement voltage from the solar panel .
SOLUTION: WE USED ADC PIN CHANNEL 10 FOR MEASUREMENT OF VOLTAGE. ACTUALLY IT IS GIVEN FOR ATTACHMENT OF EXTRA SHARP IR SENSORS.
4) The FOURTH challenge faced was due to dc motor. As the power delivered FROM THE BATTERY CHANGES CONTINUOUSLY,WE HAVE TO CHANGE DELAY TIME ACCORDINGLY.
Solution: we are using auxiliary power. We have calculated the delay time for this.

## Slide 9: Challenges & solutions
5) White line sensitivity:
in presence of high intensity (sunlight) bot sometimes does recognise the nodal point.
SOLUTION:

## Slide 10: Future work
the project can be extended to:
the bot can be used to charge the battery of mobile phones with some additional implementations.
the bot can charge itself while doing other implementation. eg: during irrigation, the bot used for watering plants can be used to charge itself.